1) Open a browser, and log in to the HMC gui.

2) In the left hand window, select:

System Management > Servers > Machine That Has The LPAR

3. The upper, right hand pane should now contain a list of the servers that machine has.

Select the LPAR to which you want to add the virtual ethernet connection.

4. In the lower, right hand pane, go to:

Configuration > Manage Profiles

A window entitled "Managed Profiles -- LPARName" will pop up with the profiles for that LPAR listed.

5. In the window that appears, select the profile to which you want to add the virtual ethernet ports.

After, from the drop down menu, select:

Actions > Edit

6. A window will appear with tabs listing various parameters that can be set, and altered.  See example below.

In it, select the "Virtual Adapters" tab.

7. From the drop down menu in the upper left hand corner, select:

Actions > Create > Ethernet Adapter

8. A window labeled "Create Virtual Ethernet Adapter: ..." will appear.

In it,

1) update the "VLAN ID" value to be on the VLAN you want the machine to communicate on.

2) Check off "This adapter is required for partition activation."

Click:

OK

9. The window will disappear, and bring you back to the window with the "Virtual Adapters" tab open.

Please note: The new virtual ethernet adapter should now be listed.

Click:

OK

10. The window will disappear bringing you back to the "Managed Profiles ..." window.

Click:

Close