Link aggregation allows you to take 2 physical, ethernet ports, and join them together to form 1 virtual, ethernet port.  This means that you will have redundancy in case 1 of the physical ports, or cables has an issue.  It also allows you to have more bandwidth for the ip address that you assign to the virtual, ethernet port than you could get from 1 physical port.

The only requirement is that both physical ports be connected to the same switch.

TO CREATE A LINK AGGREGATED, VIRTUAL PORT:

1. As padmin, to create a "link aggregation" using the physical, ethernet ports ent4 & ent5:

$ mkvdev -lnagg ent4 ent5

ent16 Available

en16

et16

$

Why ent16?  Because, when the virtual, ethernet port is created, the OS uses the next available port.  In our case, ent0 - ent15 were already created on the system.

TO VIEW WHICH ETHERNET PORTS ARE LINK AGGREGATIONS:

1. As padmin,:

lsdev | grep -i link

Example:

$ lsdev | grep -i link

ent13            Available   EtherChannel / IEEE 802.3ad Link Aggregation

$

TO FIND OUT THE REAL, PHYSICAL, ETHERNET PORTS A LINK AGGREGATE USES:

1. As padmin,:

lsdev -dev ent## -attr

Look at the line labeled: "adapter_names".

Example:

$ lsdev -dev ent13 -attr

attribute       value          description                                 user_settable

adapter_names   ent0,ent1      EtherChannel Adapters                       True

alt_addr        0x000000000000 Alternate EtherChannel Address              True

auto_recovery   yes            Enable automatic recovery after failover    True

backup_adapter  NONE           Adapter used when whole channel fails       True

hash_mode       default        Determines how outgoing adapter is chosen   True

mode            standard       EtherChannel mode of operation              True

netaddr         0              Address to ping                             True

noloss_failover yes            Enable lossless failover after ping failure True

num_retries     3              Times to retry ping before failing          True

retry_time      1              Wait time (in seconds) between pings        True

use_alt_addr    no             Enable Alternate EtherChannel Address       True

use_jumbo_frame no             Enable Gigabit Ethernet Jumbo Frames        True

$