Vhosts are used by vio servers to assign backend disks to LPARs.  Vhosts are basically just communication pipes to the LPARS.

To create a permenant pipeline from the vio server to the client LPAR, the pipeline needs to be created while both machines are down.

1. Log in to the vio server as "padmin".

2. List all the presently know vhosts.  (The command below also shows you the backend disks that are assigned to the vhost.)

lsmap -all

$ lsmap -all

SVSA            Physloc                                      Client Partition ID

--------------- -------------------------------------------- ------------------

vhost0          U9133.55A.10E4A6G-V1-C20                     0x00000003

VTD                   nimkcrootvg

Status                Available

LUN                   0x8200000000000000

Backing device        nimkc_rootvg

Physloc

VTD                   nimrootvg

Status                Available

LUN                   0x8100000000000000

Backing device        nim_rootvg

Physloc

SVSA            Physloc                                      Client Partition ID

--------------- -------------------------------------------- ------------------

vhost1          U9133.55A.10E4A6G-V1-C22                     0x00000004

VTD                   cm9112rootvg

Status                Available

LUN                   0x8100000000000000

Backing device        cm9112_rootvg

Physloc

SVSA            Physloc                                      Client Partition ID

--------------- -------------------------------------------- ------------------

vhost2          U9133.55A.10E4A6G-V1-C24                     0x00000005

VTD                   NO VIRTUAL TARGET DEVICE FOUND

SVSA            Physloc                                      Client Partition ID

--------------- -------------------------------------------- ------------------

vhost3          U9133.55A.10E4A6G-V1-C26                     0x00000006

VTD                   NO VIRTUAL TARGET DEVICE FOUND

SVSA            Physloc                                      Client Partition ID

--------------- -------------------------------------------- ------------------

vhost4          U9133.55A.10E4A6G-V1-C28                     0x00000007

VTD                   NO VIRTUAL TARGET DEVICE FOUND

SVSA            Physloc                                      Client Partition ID

--------------- -------------------------------------------- ------------------

vhost5          U9133.55A.10E4A6G-V1-C30                     0x00000008

VTD                   NO VIRTUAL TARGET DEVICE FOUND

SVSA            Physloc                                      Client Partition ID

--------------- -------------------------------------------- ------------------

vhost6          U9133.55A.10E4A6G-V1-C32                     0x00000009

VTD                   NO VIRTUAL TARGET DEVICE FOUND

$

3. Shutdown the vio server by:

hostname (Make sure you are on the correct vio server.)

who (Make sure no one is on the vio server.)

oem_setup_env

shutdown -F

4. Log in to the client LPAR as root.

5. Shut down the LPAR:

hostname (Make sure you are on the correct LPAR.)

who (Make sure no one is on the LPAR.)

shutdown -F

6. On a web broswer, log in to the HMC that controls this machine.

In the left pane, choose:

System Management > Servers > Server That Has The LPAR

7. The right pane will adjust to show you the LPARs on that server.

Select the vio server on which you are creating the vhost.

6. In the bottom part of the right pane, under "Tasks:vio server",

select:

Configuration > Manage Profiles

A window labeled "Managed Profiles -- vio server" will appear.

7. In it, select:

the profile to which you want the vhost to be added

In our example we are using "normal".

8. From the drop down menu in the upper left hand, select:

Edit...

A window will appear with various tabs to make changes to the configuration.

9. In it, select the tab:

Virtual Adapters

The tab will open listing all the virtual adapters known to this profile of the vio server.

Scroll to the bottom of the listing, and look for the last entry of "Type": "Server SCSI".  Note the values in these 2 fields:

Adapter ID

Connecting Adapter

What these 2 fields mean:

The vhost (the communication pipe) has 2 ends.  One end connects to the vio server.  The "Adapter ID" is this end.  The other end connects to the client LPAR.  The "Connecting Adapter" is this end.

In our example, the last "Server SCSI" has an "Adapter ID" of "32".  This is a virtual scsi adapter.  On the server, the virtual scsi "32" will be known to connect to the pipe to the client LPAR.  On the client, the virtual scsi adapter, "Connecting Adapter", used is "32".  This means that, on the client, the virtual scsi adapter with the ID of "32" will connect back to the vio server through the vhost communication pipe.

To make life easier when managing the vio server, and clients, we have chosen to have the adapter values on both ends be the same.  That way you only need to remember 1 number.  However, they do not need to be the same.

10. To create a new vhost (communication pipe), go to the drop down menu in the upper left hand corner.  Select:

Create > SCSI Adapter

The "Create Virtual SCSI Adapter: ..." windown will appear.

11. In it,

1) Set the "Virtual SCSI adapter Adapter" field to a value that is not being used.  (The easiest thing to do is to add 2 to the highest value previously used.  In our example, 32 was the last number used.  Therefore, 34 is the value we will use.) Note this value.  You will need it when creating the virtual scsi adapter on the client.

2) Select: "This adapter is required for partition activation.".

3) Choose: "Only selected client partiton can connect".

4) From "Client partition :", choose the client LPAR.

5) For "Client adapter ID :", enter the same value for as in 11.1.

The "Client adapter ID :" is the virtual scsi adapter on the client side.  Note this value.  You will need it when creating the virtual scsi adapter on the client.

Click:

OK

12) The window with the "Virtual Adapters" tab will reappear.

In it click:

OK

13. The "Managed Profiles" window will appear.

In it, click:

Close

14. Back at the main window,

1) unselect the vio server.

2) select the client lpar.

15. Choose:

Configuration > Manage Profiles

16. A window labeled "Managed Profiles ..." appear displaying all the profiles for the client LPAR.

Select:

the profile you want the vhost to be added to

17. From the drop down menu in the upper left, choose:

Edit...

18. A window will appear various tabs to make changes to the configuration.

In it, select the tab:

Virtual Adapters

19. The "Virtual Adapters" tab appears.

In it, from the upper left hand corner's drop down menu, choose:

Create > SCSI Adapter...

20. A window will appear allowing you to create a new, client virtual SCSI adapter.

21. In the window, set the following value:

1) For "Virtual SCSI adapter Adapter :", enter the value you  decided to use in 11.5 above.

2) Check off "This adapter is required for partition activation."

3) For "Server partition :", select the vio server we are working on.

4) For "Server adapter ID:", enter the value of the scsi adapter we created in 11.1.

Click:

OK

22. The window with the "Virtual Adapters" tab will reappear.

In it, notice that the new "Client SCSI" adapter is listed (Adapter ID: 34).

Click:

OK

23. The "Managed Profiles ..." window will reappear.

In it, from the drop down menu, select:

Activate...

24. The "Activate Logical Partition:..." window will appear.

In it, select:

the client profile we are working on

Click:

OK

25. Back at the main window,

1) Unselect the client LPAR

2) Select the vio server

26. From the bottom, right pane, select:

Operations > Activate

27. A window will appear to activate the vio server.

In it, select:

the vio server profile that you worked on

Click:

OK

28. When the vio server is up, and running, log in to it as "padmin".

29. Look at the mappings:

lsmap -all | tail

Notice, at the bottom,:

1) the new vhost "vhost7"

2) The "-C34" stands for the scsi adapter ID on the vio server we created.

3) That no backend disks are yet assigned.

$ lsmap -all | tail

vhost6          U9133.55A.10E4A6G-V1-C32                     0x00000009

VTD                   NO VIRTUAL TARGET DEVICE FOUND

SVSA            Physloc                                      Client Partition ID

--------------- -------------------------------------------- ------------------

vhost7          U9133.55A.10E4A6G-V1-C34                     0x00000000

VTD                   NO VIRTUAL TARGET DEVICE FOUND

$