1) Open a web browser, and go to IBM's fix central:

http://www-933.ibm.com/support/fixcentral/

You will be brought to the following page:

2) In the field

"Product Group",

select the product type.

In our example, we are working with p-series.  So, we select "System p".

Click:

"Continue".

3) A new drop down menu called "Product" will appear.

Select:

"Firmware and HMC".

Click:

"Continue".

4) A new drop down menu "Processor type" will appear.

In the drop down, select your processor type.

Click:

"Continue".

In our example, we are working with Power 5 CPUs.  Therefore, we select "POWER5 and POWER6 class".

5) A new drop down menu "Machine Type-Model" will appear.

Select your computer model from the drop down.

Click:

"Continue".

In our example, we select "9133-55A".

6) You will be brought to a new window confirming your model type, and asking you what types of downloads you want.

In it, select:

"System firmware.  Obtain system firmware only. ...".

Click:

"Continue".

7) You will be brought to the following screen which asks you if you need guidance.

In it, select:

"I know what I want.  I am looking for a specific ...".

Click:

"Continue".

8) A new drop down menu "Installed lsmcode" will appear.

9) Log in to any active LPAR on the machine you want to update the firwmare on.

10) Become root by one of the following methods.

1) sudo su - root

2) su - root

3) oem_setup_env (If you logged in to the vio server.)

11) As root, type:

lsmcode -c

Notes:

1) "lsmcode" tells you the firmware for the physical box.

2) The "-c" displays the output on the command line instead of putting you into a menu.

3) We are interested in the "current temporary system firmware image".

Example:

# lsmcode -c

The current permanent system firmware image is SF240_219

The current temporary system firmware image is SF240_358

The system is currently booted from the temporary firmware image.

#

What this output says is that "SF240_358" is installed as the firmware.  However, because it is temporary, you can back it out, and go back to "SF240_219", the permanent version of the firmware.

12) Back at the ibm website page,

from the drop down, select:

"Your temporary firmware level".

Click:

"Continue".

13) You are brought to a new screen asking you to select the firmware family level you want to go to.

In the drop down, select:

"The new family firmware level".

In our example, we want to go to "SF240_382".  Therefore, the family firmware level is: "SF240".

Click:

"Continue".

14) You may receive a warning message like the following.

The warning means that moving from your current firmware to your new firmware will reboot the box.  The reboot will occur during the firmware update.  Thus, all the LPARs will automatically be shut down at the time the box is rebooted.

Click:

"Continue".

15) You will be brought to a new window listing all the firmware updates you can install.

16) Scroll down until you find the one you want to install.

In the section for your new firmware, check:

"System firmware".

Click:

"Continue".

17) You will be brought to a new window asking you to confirm the license agreement.

Click:

"I agree".

18) You may receive another warning that the install of the firmware will reboot the box.

Click:

"Continue".

19) You are now brought to a screen asking you how you would like to download the firmware.

In it, select:

"Download ISO image to burn to CD".

Click:

"Continue".

20) An "Processing Order" window will appear.

21) Eventually, that window will be replaced by a new one called "Download ISO images to burn to CD-Rom".

Click:

"Download".

(This document assumes that you have enough free space on you laptop, or PC to hold the ISO images.)

22) A pop up window will appear.

In it, select the default of:

"Save File".

Click:

"OK".

23) Depending on your browser, you will get some window showing the download progress.

24) You are now done, and can close any windows used in the process.