PLEASE NOTE:

A) This procedure requires that each vio server be shut down one at a time.

B) This procedure assumes that you have already removed the LPAR definitions from the hmc gui that you no longer want to use.

===

1. Log in to the vio server as padmin.

2. Shut down the vio server:

oem_setup_env

shutdown

3. Once the vio server is shutdown, open a web browser, and connect to the HMC which manages the box.

4. Before we edit our profile, let us make a backup.

In the left hand window pane, choose:

Systems Management > Servers > ServerName

5. In the top, right hand window pane, select the vio server you are working on.

6. In the bottom, right hand window pane, choose:

Configuration > Manage Profiles

The "Managed Profiles" window will appear.

7. In it, select the profile you want to edit, and, from the
"Actions" drop down menu, choose:

Copy...

A "Copy Profile: ..." window will appear.

8. In it, enter a backup profile name in:

"New profile name:"

Click:

OK

9. Back at the "Managed Profiles" window,

select the profile you want to edit, and, from the
"Actions" drop down menu, choose:

Edit

A window will appear labeled "Logical Partition Properties: Profile Name @ VIO Server Name ...".

8. In it, choose the tab:

Virtual Adapters

9. Scroll to the section "Server SCSI"s listed.

10. We want to remove the "Server SCSI"s without named "Connecting Partition"s.  In our example, NIM(3) is the only named connecting partition.

To do remove them, select each "Server SCSI" one at a time, and go to the drop down menu "Actions" in the upper, left had corner.  From it, select:

Delete

When done, the listing should look something like this:

11. Click:

OK

The "Manage Profiles" window will come back.

12. From the "Actions" menu, choose:

Activate...

The "Activate Logical Partition" window will appear.

19. In it, select:

The profile you worked on.

Click:

OK

20. Once the vio server is back up, and running, open a putty session, and log in as padmin.

21. Check that the unused virtual hosts (vhosts), and the unused virtual target devices (VTDs) are gone.

$ lsmap -all

SVSA            Physloc                                      Client Partition ID

--------------- -------------------------------------------- ------------------

vhost0          U9133.55A.10E4A6G-V1-C20                     0x00000003

VTD                   nimkcrootvg

Status                Available

LUN                   0x8200000000000000

Backing device        nimkc_rootvg

Physloc

VTD                   nimrootvg

Status                Available

LUN                   0x8100000000000000

Backing device        nim_rootvg

Physloc

$

22. Repeat steps 1 - 21 on the other vio server.